## Slide 1
FPGA Contest 2019
Digital Billboard Controller
by THIRION Philippe

## Slide 2
Project abstract
The digital billboard controller enables to display still images on a VGA monitor. The device contains a programming interface (SPI) mainly to load images in board memory. When an image is stored in memory, the programming interface could be disconnected from the system.
It’s possible to load up to two different images in memory. A programming bit (PAGE) enables to switch between the images for displaying. This feature allows to load a new image while the current one is displayed.
Another feature is to disable display. The screen is black but the synchronization signals continue to be present. This feature is activated after system reset and avoid displaying random image before loading the first image in memory. The usage is to deactivate a programming bit (BLANKING) after loading the first image.
Notes: Notes: Please write a short summary of your idea, the concept, realization and result (current status) of the project. Make it short and use only this slide, feel free to add an image if you like

## Slide 3
Project presentation

## Slide 4
Project idea
Displaying on screen information without using a dedicated computer.
  Computer is only use to access programming interface for loading images.
Examples of use:
  Restaurant menu display
  Trade exhibition display
  ...
Better understanding how to use on board SDRAM.
Notes: Notes: tell us why you want to realize this idea and how you get the idea? Is there a use-case or just for fun?

## Slide 5
Project concept
The project uses an Arrow MAX1000 board which contains a MAX10 10M08SA device.
VGA format is the standard 640x480 at 60 Hz. Color depth is limited to 256 values.
The FPGA ‘s on chip memory is limited to 378 Kbit. To store an image, we need 2457600 bit (640 x480 x 8). In conclusion, the internal memory size is not sufficient. Fortunately, MAX1000 board includes 64 Mbit SDRAM. Then it would be possible to store up to 25 different images. The need for this project is only to store two different images.
The FPGA contains three main blocks:
  SDRAM controller with multi master AVALON-MM bus.
  A programming interface to enable accesses to SDRAM, to a controller register or to read a status register.
  A display interface, to read pixel information in the SDRAM and output VGA signals.
LEDs management block is also included to show activity (SPI accesses …).
An “on chip” PLL allows to generate a pixel clock (at 25.2 MHz) and two ram clocks (at 72 MHz).
Notes: Notes: Explain from Engineer to Engineer the concept of the project. Diagrams can be useful and technical specification are welcome

## Slide 6
Project realization
I needed to design:
  A self-made board to link the RGB FPGA outputs to a standard VGA connector.
  A QSYS module with SDRAM controller and two AVALON-MM pipeline bridges
    One for display interface (read only, eight bit burst).
    Another for programming interface (read and write).
  A display interface with two FIFOs
    An eight words (16 bit) FIFO for storing burst data.
    Another FIFO to solve clock domain crossing.
  A SPI slave programming interface to access
    The SDRAM.
    The status and control registers.
Notes: Notes: write how you realized the programming, connect external hardware and challenges you had to solve.
Can be more then 1 slide

## Slide 7
Project status
the project was tested using an
  Arduino due with an issue to store two images inside the Arduino flash (512kb). The issue was solved in Arduino compressing images with RLE algorithm.
  Raspberry Pi. A PYTHON program enables to handle GIF or PNG images and manage automatically switching between images.
Notes: Notes: show the result or current status of the projects and outlook, either for usage or what will be next steps. Even unfinished running project can win!

## Slide 8
GITHUB resources
https://github.com/tirfil/digital_billboard
  A detailed documentation (.pdf).
  The quartus archive file of the project (.qar)
  VHDL code (already available in the qar file)
  FPGA test benches + scripts (for GHDL).
  Python preprocessing code for Arduino.
  Arduino code.
  Python code for the Raspberry pi target
Notes: Notes: tell us why you want to realize this idea and how you get the idea? Is there a use-case or just for fun?

## Slide 9
Thank You